## Slide 1: Lab 1

## Slide 2
Copy Simulation/ Assignment Folder
Install Cisco Packet Tracer
Open file “Internet Simulation.pkt”

## Slide 3: Connection
PC (Fast Ethernet: 100Mbps)  Straight – through  Modem (Fast Ethernet)
PC  Desktop  IP Configuration  DHCP (get dynamic IP)
PC  Command Prompt  ping 8.8.8.8
nslookup gmail.com
nslookup ronglon.cu.to
PC  Web Browser  enter ronglon.cu.to

## Slide 4
Wireless Devices  WRT300N
WRT300N (Internet)  Straight-through  Modem (Fast Ethernet: Port 1)
WRT300N (Ethernet)  Straight-through  PC (Fast Ethernet)
PC/ Smart Phone/ Tablet/ Laptop  Desktop  IP  DHCP
Check Internet connection by using commands: ping and nslookup

## Slide 5: Email configuration
PC  Email  Configure mail
Your name: Tên gì cũng được Ví dụ: XXX
Email address: user01@gmail.com
Incoming server: 8.8.8.10
Outgoing server: 8.8.8.10
Username: user01
Password: 123456
Click Save //similarly for laptop

## Slide 6: Send/ receive emails
PC/ Laptop  Email  Mail Browser  Compose
E.g.: send email from Laptop to PC (user02  user01)
To: user01@gmail.com
Subject: Gì cũng được Ví dụ: Tra sua khong em
Hen em 9h 6p
Click Send
-------------------------------------------------------------------------------
PC: receive mail from Laptop
PC  Email  Mail Browser  Receive

## Slide 7
Modem (Fast Ethernet)  Crossover  Switch (Fast Ethernet)
Switch (Fast Ethernet)  Straight-through  Generic Access Point
Switch (Fast Ethernet)  Straight-through  PC (Fast Ethernet)
PC/ Laptop/ Smart phone/ Tablet  IP  DHCP
Có sự khác biệt gì giữa 2 sơ đồ (dùng WRT300N và GENERIC)?
WRT300N: 192.168.0.0/24
GENERIC: 6.9.6.0/24 (get IP from ISP)