## Slide 1: Lab 3

## Slide 2: Infrastructure: Router, Switch & End devices
1841 Router  Click  Turn off  Drag and Drop 2 WIC-1ENET  Turn on
1841 Router (F0/0) <--- Straight-through ---> Modem (Port 1)
Subnet 0 (students):
1841 Router (F0/1) <--- Straight-through ---> Switch 2950 (cổng nào cũng được)
Server (FastEthernet) <--- Straight-through ---> Switch 2950 (cổng nào cũng được)
Wireless GENERIC <--- Straight-through ---> Switch 2950 (cổng nào cũng được)
Laptop/ Smartphone/ Tablet
Subnet 1 (Labs):
1841 Router (E0/0/0) <--- Straight-through ---> Switch 2950 (cổng nào cũng được)
Server (FastEthernet) <--- Straight-through ---> Switch 2950 (cổng nào cũng được)
PC <--- Straight-through ---> Switch 2950 (cổng nào cũng được)
Similarly to Subnet 2 (office): 1841 Router (E0/1/0)

## Slide 3: DHCP Server (Dynamic Host Configuration Protocol)
Subnet 0  Click Server  Desktop  IP Configuration  enter designed parameters (IP: 172.16.0.2/23, DG: 172.16.0.1, DNS: 8.8.8.8)  Close
Server  Services  DHCP  On
Default gateway : 172.16.0.1
DNS : 8.8.8.8
Start IP: : 172.16.0.3
Subnet Mask : 255.255.254.0
Maximum users : 369
Save
Click PC/ Laptop/ Smart phone  Desktop  IP Configuration  DHCP to check
Similarly to Subnet 1 & 2